## Slide 1
MicroMouse
Robot
Autonomous Maze-Solving Robot
ESP32 · LiDAR · Flood-Fill BFS · PD Control · WiFi
Interfacing Techniques · Academic Year 2025–2026 · February 28 2026
Team : Aya Fares, Nagham Massis, Alzahra Nassif, Marah Hamarsheh
Supervised by: Dr. Wasel Ghanam
Notes: Title slide. MicroMouse autonomous maze-solving robot project — Interfacing Techniques course 2025–2026.

## Slide 2
Project Overview
What is MicroMouse? What did we set out to build?
MicroMouse System
What is MicroMouse?
An autonomous robot that navigates and solves an unknown 16×16 maze as fast as possible. A classic IEEE robotics competition since 1977. No human control once started.
3 VL53L0X LiDAR sensors
Flood-Fill BFS algorithm
PD motor control loops
ESP32 dual I²C bus setup
Gyroscope accurate turns
Live WiFi tuning dashboard
2
Notes: Project overview: what MicroMouse is and our 6 core technical goals.

## Slide 3
Project Management — Trello Board
How we organized our entire workflow
PLAN — Main Timeline
6 phases tracked end-to-end
Hardware Components
All parts with photos & receipts
UPCOMING Next Tasks
Always-visible next actions
CRITICAL REMINDERS
Lab bookings, backups, tests
Testing Videos
Algorithm comparison recordings
3
Notes: Trello was used to manage the entire project. Show how each list tracked a different aspect of the workflow.

## Slide 4
Project Timeline — 6 Phases
December 2025 → February 2026
Dec 25
01
Research
Studied MicroMouse competitions, algorithms, sensor options
Dec 25
02
Design
Designed the alpha version and optimized robot geometry using Autodesk Fusion.
Dec 25
03
Hardware
Component evaluation & purchase. All 10 parts selected
Jan 26
04
3D Printing
Jan 26
05
Mechanical
Booked lab, printed chassis, motor mounts, sensor brackets
Feb 26
06
Software & Test
Flood-Fill, PD control, WiFi dashboard, full maze tests
4
Wiring, I²C buses, motor driver, PCB layout
Notes: 6 phases from December 2025 to February 2026. Each phase tracked on Trello.

## Slide 5
Hardware Components — Complete Bill of Materials
All 10 components selected, purchased and verified
ESP32-WROOM-32
Microcontroller
ESP32 Expansion Shield
Pin Breakout Board
DC Gear Motor + Encoder
Drive System × 2
L298N Motor Driver
H-Bridge PWM Control
VL53L0X LiDAR × 3
Time-of-Flight Sensor
MPU6050 IMU
Gyroscope + Accel
Li-ion Battery 9V
Rechargeable Power
DC-DC Boost Converter
Voltage Regulator
On/Off Power Switch
Power Control
Jumper Wires
M-M / M-F / F-F Connections
5
Notes: All 10 hardware components with photos. Each tracked as a card in the Trello Hardware Components list.

## Slide 6
ESP32-WROOM-32 Microcontroller
The brain: dual-core 240MHz, WiFi, dual I²C buses, PWM
Expansion Shield
for clean pin access
Dual-Core 240 MHz
Runs Flood-Fill + WiFi server simultaneously without lag
Built-in WiFi
Hosts async web server, live PID dashboard, no extra module
Dual I²C Buses
Bus 0 → MPU6050 (GPIO 19/18). Bus 1 → 3× LiDAR (GPIO 5/17)
HW Interrupt Pins
GPIO 33/32 and 34/35 count encoder pulses at high frequency
PWM (LEDC)
GPIO 13, 25, 26 generate PWM for L298N motor speed control
3.3V Logic — Critical
All sensors/drivers must stay ≤3.3V. Exceeded → burned chip!
6
Notes: ESP32 is the central MCU. Key features: dual-core, WiFi, dual I²C, hardware interrupts for encoders, PWM for motors. The 3.3V limit is critical — we burned one unit by exceeding it.

## Slide 7
Component — VL53L0X LiDAR Sensors × 3
The eyes: Time-of-Flight laser ranging for wall detection
FRONT
LEFT
RIGHT
Sensor Technology Comparison
Property | IR Sensor | Ultrasonic | VL53L0X
Accuracy | ±10–50 mm | ±5 mm | ±1–2 mm
Field of View | Wide / noisy | Wide / echo | Narrow 25°
Light Immune | No | Yes | Yes
I²C Interface | No | No | Yes
Best For | Simple presence | Open space | Precise walls
FRONT SENSOR
Detects wall ahead. Triggers stop or turn decision. Threshold: < 150mm = wall present.
LEFT SENSOR
Checks left wall. Decides if left turn is possible. XSHUT pin cycles address at boot.
RIGHT SENSOR
Checks right wall. All 3 share I²C Bus 1 with unique addresses assigned via XSHUT pins.
7
ROBOT
Notes: Three VL53L0X LiDAR sensors provide wall detection front, left, and right. LiDAR was chosen over IR/ultrasonic for its ±1–2mm accuracy and clean I²C interface.

## Slide 8
Component — Motors, Encoders & Motor Driver
Locomotion: DC gear motors + quadrature encoders + L298N H-bridge
DC Gear Motor
+ Quadrature Encoder
L298N Dual
Motor Driver
PD Control Loop
Encoder
Counts
Speed
Error
P+D
Correction
PWM
Output
Straight
Motion
Quadrature Encoders
4 pins (A+B per motor) → ESP32 GPIO 33/32 & 34/35. Interrupt-driven pulse counting for precise odometry.
H-Bridge Direction
IN1–IN4 pins control forward/reverse per motor independently. Each motor fully bidirectional at all speeds.
PWM Speed Control
ESP32 LEDC peripheral generates PWM on GPIO 13, 25, 26. Duty cycle 0–100% controls velocity smoothly.
Overvoltage Lesson
Motor back-EMF spikes back-fed into ESP32 logic pins. After burn-out, added 100nF bypass capacitors on PWM lines.
8
Notes: Two DC gear motors with quadrature encoders provide drive and odometry. L298N H-bridge handles bidirectional PWM. PD controller equalizes wheel speeds using encoder feedback.

## Slide 9
Component — IMU & Power System
MPU6050 gyroscope + Li-ion battery + boost converter + switch
MPU6050 IMU
Li-ion 9V Battery
DC-DC Converter
Power Switch
MPU6050 — Gyroscope & Accelerometer
I²C Bus 0 (GPIO 19/18). Provides gyroZ_raw → accumulated over time to track currentYaw. Enables accurate 90°/180° turns without encoder wheel-slip drift. Also provides accelerometer for motion state detection.
Li-ion Rechargeable 9V Battery
Main power source for the entire robot. USB-C charging. Stable current delivery during motor load spikes. We kept backup batteries after the burn-out incident (tracked on Trello Critical Reminders).
Step-Up DC-DC Boost Converter
Adjustable output voltage. Regulates battery voltage to stable levels for motors and logic rails. Protects ESP32's 3.3V logic rail from motor voltage fluctuations and back-EMF spikes.
On/Off Rocker Switch
Inline with battery circuit. Allows safe power on/off without disconnecting wires. Critical for our staged power-on testing protocol — always verify voltages before connecting ESP32.
9
Notes: IMU provides gyroscope data for accurate turning. Power system includes battery, boost converter for stable voltage, and a switch for safe power-on procedures.

## Slide 10
Mechanical Design & 3D Printing
Phase 4 & 5: chassis, sensor mounts, motor brackets, final assembly
Design Specifications
Size
13X13 cm footprint - fits maze that it size 19.5x19.5
Material
PLA plastic — rigid, lightweight, printable
Drive
2 DC motors, rear-positioned, differential drive
Sensors
Front center + left/right 45° angled LiDAR mounts
Weight
Minimized — faster acceleration & turning
PCB
ESP32 shield top-center for WiFi antenna clearance
Battery
Li-ion mounted low for stable center of gravity
Switch
Accessible on chassis side for safe power-on
15
Notes: Mechanical design used CAD + 3D printing. Two iterations needed for correct motor mount tolerances. Lab bookings tracked on Trello.

## Slide 11
System Overview — All Components & Wiring
Every GPIO connection from the actual code
ESP32-WROOM-32
Dual-Core 240MHz | WiFi
VL53L0X FRONT
XSHUT→GPIO 16 | I²C addr 0x30
VL53L0X LEFT
XSHUT→GPIO 17 | I²C addr 0x31
VL53L0X RIGHT
XSHUT→GPIO 4 | I²C addr 0x32
MPU6050 IMU
Wire.begin(21, 22) — I²C SDA/SCL
Motor A + Encoder A
ENA=25 IN1=27 IN2=14 | ENC_A1=32 ENC_A2=33
Motor B + Encoder B
ENB=26 IN3=12 IN4=13 | ENC_B1=18 ENC_B2=19
L298N Motor Driver
spinRight/Left/setForward | turnPWM=85
Li-ion + Boost + SW
9V battery → DC-DC regulator → power switch
10

## Slide 12
Complete Pinout
Every ESP32 GPIO connection verified against #define constants in the firmware
Component | GPIO Pin(s) | Protocol | Function (from code)
I²C — MPU6050 IMU |  |  | 
MPU6050 SDA | GPIO 21 | I²C (Wire.begin) | IMU data line — Wire.begin(21, 22)
MPU6050 SCL | GPIO 22 | I²C (Wire.begin) | IMU clock line — Wire.begin(21, 22)
I²C — VL53L0X LiDAR × 3 (shared bus) |  |  | 
LiDAR SDA (all 3) | GPIO 21 | I²C (Wire) | All 3 sensors share same I²C bus as MPU6050
LiDAR SCL (all 3) | GPIO 22 | I²C (Wire) | Same Wire bus — unique addresses via XSHUT
XSHUT FRONT | GPIO 16 | Digital Output | XSHUT_FRONT — boots sensor, assigns 0x30
XSHUT LEFT | GPIO 17 | Digital Output | XSHUT_LEFT — boots sensor, assigns 0x31
XSHUT RIGHT | GPIO 4 | Digital Output | XSHUT_RIGHT — boots sensor, assigns 0x32
MicroMouse · Interfacing Techniques · Pinout

## Slide 13
Encoders — Quadrature (IRAM_ATTR ISRs) |  |  | 
Left Encoder ISR | GPIO 32 | Interrupt (RISING) | ENC_A1 — RISING edge triggers encoderA_ISR
Left Encoder Dir | GPIO 33 | Digital Input | ENC_A2 — read in ISR: HIGH=forward LOW=back
Right Encoder ISR | GPIO 18 | Interrupt (RISING) | ENC_B1 — RISING edge triggers encoderB_ISR
Right Encoder Dir | GPIO 19 | Digital Input | ENC_B2 — read in ISR: HIGH=forward LOW=back
Motor Driver L298N — Speed + Direction |  |  | 
Motor A Speed (ENA) | GPIO 25 | PWM analogWrite | ENA — Motor A speed 0–255 duty cycle
Motor A Dir IN1 | GPIO 27 | Digital Output | IN1 — setForward: LOW ¦ spinRight: HIGH
Motor A Dir IN2 | GPIO 14 | Digital Output | IN2 — setForward: HIGH ¦ spinRight: LOW
Motor B Speed (ENB) | GPIO 26 | PWM analogWrite | ENB — Motor B speed 0–255 duty cycle
Motor B Dir IN3 | GPIO 12 | Digital Output | IN3 — setForward: LOW ¦ spinLeft: HIGH
Motor B Dir IN4 | GPIO 13 | Digital Output | IN4 — setForward: HIGH ¦ spinLeft: LOW
Continue - Pinout
Component | GPIO Pin(s) | Protocol | Function (from code)

## Slide 14
Algorithm Selection — Evaluating 4 Approaches
Why we chose Flood-Fill BFS for unknown maze navigation
Wall Follower
Rejected
Pros:
Simple to code
Very low memory
Cons:
– Gets stuck in loops
– Cannot solve all maze types
– Non-optimal path
Dijkstra / A*
Rejected
Pros:
Optimal path
Works on known maps
Cons:
– Needs full map
– Heavy for ESP32 RAM
– Not for unknown maze
Flood-Fill BFS
CHOSEN ✓
Pros:
Only 16×16 int array
Dynamic — adapts to new walls
Fast BFS re-flood
Efficient on microcontroller
Explores unknown maze well
Cons:
– Re-floods on new wall
– Slightly complex code
11
Notes: Four algorithms compared. Flood-Fill was chosen for its efficiency, dynamic adaptability, and minimal memory use — perfect for unknown-maze navigation on a constrained MCU.

## Slide 15
Pin Definitions
Every #define and global variable declaration
/* ====== MOTOR PINS ====== */
#define ENA 25 // Motor A speed (PWM)
#define IN1 27 // Motor A direction
#define IN2 14
#define ENB 26 // Motor B speed (PWM)
#define IN3 12 // Motor B direction
#define IN4 13
/* ====== ENCODER PINS ====== */
#define ENC_A1 32 // ISR trigger (RISING)
#define ENC_A2 33 // direction pin
#define ENC_B1 18 // ISR trigger (RISING)
#define ENC_B2 19 // direction pin
/* ====== XSHUT PINS ====== */
#define XSHUT_FRONT 16
#define XSHUT_LEFT 17
#define XSHUT_RIGHT 4
/* ====== GLOBALS ====== */
volatile long countA = 0, countB = 0;
float gz_bias = 0.0f;
float yaw = 0.0f;
int posX = 0, posY = 0;
int heading = NORTH;
Motor A: ENA + IN1/IN2
→ ENA GPIO 25 → analogWrite() PWM speed control
→ IN1 GPIO 27 + IN2 GPIO 14 → forward/reverse
→ setForward(): IN1=LOW, IN2=HIGH
→ spinRight(): IN1=HIGH, IN2=LOW
Motor B: ENB + IN3/IN4
→ ENB GPIO 26 → analogWrite() PWM speed control
→ IN3 GPIO 12 + IN4 GPIO 13 → forward/reverse
→ setForward(): IN3=LOW, IN4=HIGH
→ spinLeft(): IN3=HIGH, IN4=LOW
Encoders — IRAM_ATTR ISR
→ ENC_A1 GPIO 32 → RISING edge triggers encoderA_ISR
→ ENC_A2 GPIO 33 → read for direction: HIGH=++ LOW=--
→ ENC_B1 GPIO 18 → RISING edge triggers encoderB_ISR
→ ENC_B2 GPIO 19 → direction for Motor B
LiDAR XSHUT — Address Boot
→ GPIO 16 FRONT → init() → setAddress(0x30)
→ GPIO 17 LEFT → init() → setAddress(0x31)
→ GPIO 4 RIGHT → init() → setAddress(0x32)
→ All 3: setTimeout(250) ms

## Slide 16
Encoder ISRs & Gyroscope Calibration
IRAM_ATTR interrupt handlers + 800-sample calibrateGyro()
// Encoder ISRs — stored in IRAM
void IRAM_ATTR encoderA_ISR(){
if (digitalRead(ENC_A2)) countA++;
else countA--;
}
void IRAM_ATTR encoderB_ISR(){
if (digitalRead(ENC_B2)) countB++;
else countB--;
}
void calibrateGyro() {
const int N2 = 800;
float sum = 0;
for(int i=0; i<N2; i++){
sum += readGz();
delay(3); // 800 × 3ms = 2.4s
}
gz_bias = sum / N2;
}
// In loop — integrate yaw every tick:
float gz = readGz() - gz_bias;
yaw += gz * dt; // rad/s × seconds
IRAM_ATTR — Why Critical
IRAM_ATTR places the ISR in internal SRAM. Without it, ESP32's flash cache misses during WiFi/SPI activity cause the ISR to stall — losing encoder pulses at high speed. Essential for reliable tick counting.
Quadrature Direction Logic
On every RISING edge of ENC_A1, the ISR immediately reads ENC_A2:
• HIGH → wheel moving forward → countA++
• LOW → wheel moving backward → countA--
Same logic mirrors for Motor B via ENC_B2.
Gyro Calibration — 800 samples
800 samples × 3ms delay = 2.4 seconds of robot stillness at startup. Averages raw gz readings to compute gz_bias. Every future readGz() call subtracts this bias to eliminate zero-offset drift.
Yaw Integration
Each loop: float gz = readGz() - gz_bias; yaw += gz * dt;
The dt guard (if dt < 0.005f return) ensures minimum 5ms between corrections — prevents noise amplification from extremely fast dt values.
4

## Slide 17
LiDAR Setup - setupSensors() with XSHUT Cycling
All 3 VL53L0X sensors start at address 0x29 — sequential boot assigns unique addresses
void setupSensors() {
pinMode(XSHUT_FRONT, OUTPUT);
pinMode(XSHUT_LEFT, OUTPUT);
pinMode(XSHUT_RIGHT, OUTPUT);
// Pull ALL sensors into hardware reset
digitalWrite(XSHUT_FRONT, LOW);
digitalWrite(XSHUT_LEFT, LOW);
digitalWrite(XSHUT_RIGHT, LOW);
delay(10);
// Wake FRONT, init, assign 0x30
digitalWrite(XSHUT_FRONT, HIGH); delay(10);
frontSensor.init();
frontSensor.setAddress(0x30);
// Wake LEFT, init, assign 0x31
digitalWrite(XSHUT_LEFT, HIGH); delay(10);
leftSensor.init();
leftSensor.setAddress(0x31);
// Wake RIGHT, init, assign 0x32
digitalWrite(XSHUT_RIGHT, HIGH); delay(10);
rightSensor.init();
rightSensor.setAddress(0x32);
frontSensor.setTimeout(250);
leftSensor.setTimeout( 250);
rightSensor.setTimeout(250);
}
Why Sequential Booting?
All 3 VL53L0X sensors share the same default I²C address (0x29). XSHUT = LOW forces hardware reset, keeping a sensor silent. Only the active sensor is visible on the bus during address assignment.
1
ALL → RESET (LOW)
All 3 XSHUT pins pulled LOW simultaneously. All sensors enter hardware reset — none respond to I²C.
2
FRONT → HIGH (0x30)
Only FRONT wakes up. frontSensor.init() communicates at default 0x29. setAddress(0x30) → FRONT now lives at 0x30 permanently.
3
LEFT → HIGH (0x31)
LEFT wakes up. leftSensor.init() at 0x29 (FRONT is at 0x30, no collision). setAddress(0x31) → LEFT locked at 0x31.
4
RIGHT → HIGH (0x32)
RIGHT wakes up. rightSensor at 0x29. setAddress(0x32). Now all 3 sensors on same bus: 0x30, 0x31, 0x32. setTimeout(250ms) each.
5

## Slide 18
Flood-Fill — initFlood(), floodFill(),
selectDirection()
8×8 maze with 4 goal cells at (3,3)(3,4)(4,3)(4,4)
8×8 Flood Grid — Manhattan dist to 4 goals
S
5
4
3
3
4
5
6
5
4
3
2
2
3
4
5
4
3
2
1
1
2
3
4
3
2
1
G
G
1
2
3
3
2
1
G
G
1
2
3
4
3
2
1
1
2
3
4
5
4
3
2
2
3
4
5
6
5
4
3
3
4
5
6
S=Start(0,0) G=Goals(3-4,3-4) GOAL_CELLS[4][2]={{3,3},{3,4},{4,3},{4,4}}
void initFlood() {
for(x=0;x<8;x++) for(y=0;y<8;y++){
int d = 9999;
for(i=0;i<4;i++) // 4 goals
d=min(d,abs(x-gx)+abs(y-gy));
flood[x][y] = d;
}
// Override: goals = 0
flood[3][3]=flood[3][4]=0;
flood[4][3]=flood[4][4]=0;
}
void floodFill() {
bool changed = true;
while(changed) {
changed = false;
for each cell (x,y):
if(!isConsistent(x,y)){
makeConsistent(x,y);
changed = true;
}
} // repeat until stable
}
int selectDirection(x,y,h){
int bestDir=-1,bestF=9999;
int bestUnk=-1,fallback=-1;
// prev cell = avoid backtrack
int px=x-dirs[h][0];
for(d=0; d<4; d++){
if(!isAccessible...) skip;
if(nx==px&&ny==py){
fallback=d; continue;
}
int fval=flood[nx][ny];
int unk =unknownScore(nx,ny);
if(fval<bestF ||
(fval==bestF && unk>bestUnk))
bestDir=d; // pick it
}
if(bestDir==-1) return fallback;
}
unknownScore(x,y)
Counts walls not yet set for a cell (N/E/S/W).
+1 for each wall not in maze[x][y]
Higher score → more unknown area → higher exploration priority
selectDirection: choose lowest flood value first, then highest unknown score if tied.
· 6

## Slide 19
senseWalls() — LiDAR Reading → Maze Map Update
Translating sensor readings to cardinal wall directions based on heading
void senseWalls(int x, int y, int h) {
int fD = readFrontDistance();
int lD = readLeftDistance();
int rD = readRightDistance();
bool wallF = (fD < wallThresholdFront); // 100mm
bool wallL = (lD < wallThresholdSide); // 120mm
bool wallR = (rD < wallThresholdSide); // 120mm
if(wallF){
if(h==NORTH) setWall(x,y,N_WALL);
if(h==EAST) setWall(x,y,E_WALL);
if(h==SOUTH) setWall(x,y,S_WALL);
if(h==WEST) setWall(x,y,W_WALL);
}
if(wallL){ // left→west if NORTH
if(h==NORTH) setWall(x,y,W_WALL);
if(h==EAST) setWall(x,y,N_WALL);
if(h==SOUTH) setWall(x,y,E_WALL);
if(h==WEST) setWall(x,y,S_WALL);
}
if(wallR){ /* mirror of wallL */ }
}
void setWall(int x,int y,int dir) {
maze[x][y] |= dir; // bitmask OR
if(dir==N_WALL&&y+1<8) maze[x][y+1]|=S_WALL; // sync neighbour
Wall Bitmask — maze[x][y]
Define | Value | Meaning
N_WALL | 1 (0001) | North ↑ wall
E_WALL | 2 (0010) | East → wall
S_WALL | 4 (0100) | South ↓ wall
W_WALL | 8 (1000) | West ← wall
Heading → Sensor → Wall Direction
Heading | FRONT | LEFT | RIGHT
NORTH | N_WALL | W_WALL | E_WALL
EAST | E_WALL | N_WALL | S_WALL
SOUTH | S_WALL | E_WALL | W_WALL
WEST | W_WALL | S_WALL | N_WALL
setWall() also updates the shared wall of the neighbour cell e.g. N_WALL on (x,y) also sets S_WALL on (x,y+1). Prevents map inconsistency.
7

## Slide 20
Main Loop — 4-Stage Execution Order
Every iteration of loop() — from the actual code structure
1
Gyro Straight-Line PD
⏱ dt < 5ms → skip (rate-limited)
float dt = (now - lastUs) / 1e6f;
if(dt < 0.005f) return; // rate limit
float gz = readGz() - gz_bias;
yaw += gz * dt;
int gyroCorr = SIGN*(Kp_yaw*err - Kd_rate*gz);
int corr = constrain(gyroCorr+wallCorr,-70,70);
pwmA = constrain(baseA-corr, 0,180); // 65
pwmB = constrain(baseB+corr, 0,180); // 55
2
Wall PD Correction
⏱ Every 30ms (was 100ms)
if(nowMs - lastSideRead > 30){
cachedLeft = readLeftDistance();
cachedRight = readRightDistance();
if(wL && wR) wallError = R - L; // both walls
if(only wR) wallError = R - centerTarget(35);
if(cachedR < dangerZone(20)) wallError=+60;
wallCorr = Kp_wall*err + Kd_wall*(err-prev);
wallCorr = constrain(wallCorr, -35, 35);
3
Front Emergency Stop
⏱ Every 80ms | frontDist < 50mm
if(nowMs - lastFrontCheck > 80){
int frontDist = readFrontDistance();
if(frontDist < 50){
stopMotors(); delay(50);
senseWalls(posX,posY,heading);
floodFill();
dir = selectDirection(...);
turnToFace(dir); resumeDriving();
4
Square Boundary Decision
⏱ Every 240 encoder ticks
long ticks = (labs(countA)+labs(countB))/2;
if(ticks - lastCheckTicks >= 240){
gradualStop(); updatePosition();
delay(squareDelayMs); // 300ms pause
senseWalls→floodFill→printFlood;
dir = selectDirection(posX,posY,heading);
if(dir!=heading) turnToFace(dir);
else resumeDriving(); // straight on
· 8

## Slide 21
Two-Layer PD Control — Gyro + Wall Centering
Layer 1: yaw heading correction. Layer 2: side-wall position correction
// === LAYER 1: GYRO (every loop ≥5ms) ===
float gz = readGz() - gz_bias;
yaw += gz * dt;
float err = 0.0f - yaw; // target yaw = 0
int gyroCorr = SIGN * (Kp_yaw*err - Kd_rate*gz);
// Kp_yaw=220.0 Kd_rate=25.0 SIGN=-1
// === LAYER 2: WALL PD (every 30ms) ===
int wallError = cachedRight - cachedLeft; //both
// single right wall:
wallError = cachedRight - centerTarget; // 35mm
if(cachedRight < dangerZone) // 20mm
wallError = dangerPush; // =60 emergency!
int wallD = wallError - prevWallError;
wallCorr = Kp_wall*wallError + Kd_wall*wallD;
// Kp_wall=1.2 Kd_wall=0.8
wallCorr = constrain(wallCorr, -35, 35);
// === COMBINE & APPLY ===
int corr = constrain(gyroCorr + wallCorr, -70, 70);
int pwmA = constrain(baseA - corr, 0, 180); // 65
int pwmB = constrain(baseB + corr, 0, 180); // 55
setForward();
analogWrite(ENA, pwmA); // GPIO 25
analogWrite(ENB, pwmB); // GPIO 26
All PD Tuning Values
Param | Value | Notes
Kp_yaw | 220.0 | Gyro P — heading correction
Kd_rate | 25.0 | Gyro D — damps oscillation
SIGN | −1 | Flip if robot curves wrong way
corrLimit | 70 | Max combined correction ±70
baseA | 65 | Motor A base PWM
baseB | 55 | Motor B base PWM (different!)
Kp_wall | 1.2 | Wall P (was 1.8 → too shaky)
Kd_wall | 0.8 | Wall D (was 2.0 → too shaky)
wallCorrLimit | 35 | Max wall corr (was 50)
centerTarget | 35mm | Target side wall distance
dangerZone | 20mm | Emergency push threshold
dangerPush | 60 | Emergency push (was 80)
Why baseA≠baseB?
Both motors are physically different. baseA=65 vs baseB=55 compensates for the constant torque imbalance. The gyro PD loop handles dynamic drift on top.
SIGN = -1
Depends on motor wiring polarity. Flip to +1 if robot curves opposite direction — no rewiring needed.
MicroMouse · Interfacing Techniques · 9

## Slide 22
turnRight90() / turnLeft90() — Encoder-Based Turns
85 ticks per 90°, balanced tick control, gradual PWM ramp-down + straightenYaw()
void turnRight90() {
stopMotors(); delay(150);
resetCountersSafe(); // detach ISR, 0, reattach
spinRight(); // IN1=H IN2=L IN3=L IN4=H
analogWrite(ENA, turnPWM); // 85
analogWrite(ENB, turnPWM); // 85
unsigned long start = millis();
while(true){
long tA=labs(countA), tB=labs(countB);
if(tA >= 85 && tB >= 85){ // turnCounts90
for(p=85;p>=0;p-=15) { // ramp down
analogWrite(ENA,p);analogWrite(ENB,p);
delay(10);
}
stopMotors(); delay(100); return;
}
// Balance ticks — keep both wheels equal
if(tA > tB+5) ENA = turnPWM*0.7; // slow A
if(tB > tA+5) ENB = turnPWM*0.7; // slow B
if(millis()-start>2000) return; // timeout
delay(2);
}
}
void gradualStop() {
int steps = 8;
for(p = steps; p >= 0; p--){
float fraction = (float)p / steps;
int curA = baseA * fraction; // baseA=65
int curB = baseB * fraction; // baseB=55
// Gyro still running during deceleration!
gz2 = readGz()-gz_bias; yaw+=gz2*dt2;
corr2 = constrain(SIGN*Kp_yaw*err2,-30,30);
analogWrite(ENA, curA-corr2);
analogWrite(ENB, curB+corr2);
delay(12); // 8 steps × 12ms = 96ms total
}
stopMotors(); delay(100);
}
resetCountersSafe()
detachInterrupt → countA=0, countB=0 → delay(10) → attachInterrupt. Prevents stale encoder ticks from last cell traversal corrupting the turn count.
Balanced Tick Control
During turn: if tA > tB+5, slow Motor A to 70% PWM. This keeps both wheels advancing at equal rates, ensuring a straight in-place rotation rather than a curved arc.
Ramp-Down (85→0 steps of 15)
When 85 ticks reached: PWM ramps 85→70→55→40→25→10→0. Each step has 10ms delay. Prevents overshoot from motor momentum — robot stops precisely at 90°.
gradualStop() — Gyro Active
8 steps of deceleration (fraction 1.0→0). Gyro PD loop remains running each step. Keeps robot heading stable while decelerating — prevents drift at cell boundaries.
turnToFace() calls straightenYaw()+fullCenter()
Before every turn: straightenYaw() uses gyro+walls to correct small heading error. fullCenter() laterally centers between walls. Only then does the 90° turn execute.
· 10

## Slide 23
setup() — Exact Initialization Order
From Serial.begin to resumeDriving() — every step from the code
void setup() {
Serial.begin(115200);
// ① Motors + Encoders
pinMode(ENA,OUT); ... stopMotors();
pinMode(ENC_A1,INPUT_PULLUP); // × 4
attachInterrupt(ENC_A1, encoderA_ISR, RISING);
attachInterrupt(ENC_B1, encoderB_ISR, RISING);
// ② I²C + LiDAR
Wire.begin(21, 22); // SDA=21 SCL=22
setupSensors(); // XSHUT → 0x30/0x31/0x32
// ③ MPU6050
if(!mpu.begin()) while(1) delay(100); // halt
mpu.setGyroRange(MPU6050_RANGE_250_DEG);
mpu.setFilterBandwidth(MPU6050_BAND_21_HZ);
// ④ Calibrate gyro — 2.4s still
delay(2000); calibrateGyro();
// ⑤ Print sensor distances
Serial.print(readFrontDistance()); // mm
// ⑥ Init maze with boundary walls
for(i=0;i<8;i++) maze[i][0] |= S_WALL;
for(i=0;i<8;i++) maze[i][7] |= N_WALL;
for(i=0;i<8;i++) maze[0][i] |= W_WALL;
for(i=0;i<8;i++) maze[7][i] |= E_WALL;
// ⑦ Flood + first decision
initFlood(); posX=0; posY=0; heading=NORTH;
doFloodDecision();
if(goalReached) while(1) delay(1000);
delay(2000); resumeDriving();
}
①
Motors & Encoders
All 6 motor pins OUTPUT. stopMotors(). ENC × 4 INPUT_PULLUP. ISRs attached on RISING.
②
Wire + LiDAR
Wire.begin(21,22). setupSensors() cycles XSHUT → addresses 0x30/0x31/0x32. 250ms timeout each.
③
MPU6050
mpu.begin() — halts on fail. Gyro range 250°/s. DLPF bandwidth 21Hz to filter vibration noise.
④
Gyro Calibration
delay(2000) for mechanical settling. calibrateGyro() takes 2.4s — computes gz_bias from 800 samples.
⑤
Sensor Self-Test
Prints Front/Left/Right distances to Serial 115200. Confirms all 3 LiDAR sensors responding before maze start.
⑥
Maze Init
maze[8][8] zeroed. Outer boundary walls set: S on row 0, N on row 7, W on col 0, E on col 7. initFlood() populates distances.
⑦
First Decision
doFloodDecision() at (0,0,NORTH): sense walls → floodFill → selectDirection → turnToFace(). 2s delay then resumeDriving().
· 11

## Slide 24
Critical Challenge - ESP32 Overvoltage Burn-Out
Our most significant setback and how we resolved it
What Happened
During hardware assembly, we damaged our ESP32 microcontroller and the I/O expander due to overvoltage.
Root Cause
Voltage exceeding the ESP32’s 3.3V logic limit reached the GPIO pins.
Motor back-EMF spikes fed back from the L298N through the PWM lines.
Why It Was Catastrophic
Once the ESP32 GPIO exceeded 3.3V, thermal runaway occurred in the silicon. The chip became permanently damaged and could not be repaired. The I/O expander was also destroyed.
Resolution Steps
· 14
Backup ESP32 Immediately added the ESP32 to our critical spares list and purchased backups.
Voltage Isolation Redesigned the power system with dedicated 5V and 3.3V rails. Isolated ESP32 logic lines from the motor supply.
Staged Power Protocol Implemented a rule to verify all voltages with a multimeter before connecting the ESP32. Powered stages sequentially.
Notes: Burning the ESP32 was our biggest setback but made our final design much more robust through proper voltage protection and staged testing protocols.

## Slide 25
Testing Strategy - Bottom-Up Validation
Unit tests → Integration tests → Full maze solving
Unit Tests
Each component alone
Gyroscope Test
Verified gyroZ_raw, calibrated zero offset, confirmed 90° detection
DC Motor Test
Tested forward/reverse at 5 speeds. Verified encoder pulses per revolution
LiDAR Test
Each VL53L0X tested individually via XSHUT cycling. Accuracy at 10/20/30cm
I²C Bus Scan
Confirmed all 4 devices at correct addresses on both buses before integration
Integration Tests
Systems combined progressively
Test 1: Straight Motion
Both motors coordinated. Verified encoder sync and ±2mm straight-line tracking
Test 2: Turn + Algorithm
Move forward, 90° gyro turn, Flood-Fill direction selection. Angle ±1° accuracy
Test 3: Closed Loop
Navigate full rectangle: fwd → right → fwd → right → back to start. Flood-Fill verified
Motion Challenges
Problems found & fixed
Straight-Line Drift
Motor speed mismatch. Fixed: encoder PD equalizes speeds every loop cycle
90° Turn Overshoot
Gyro lag caused overshoot. Fixed: dynamic yaw target recalibration + lower Kd
LiDAR Noise Spikes
False wall detections. Fixed: median filter over 3 readings + min threshold
I²C Address Conflict
2 LiDARs same address. Fixed: XSHUT cycling assigns unique addresses at boot
16
Notes: Bottom-up testing approach: each component validated independently before integration. Three phases: unit tests, integration tests, full maze runs.

## Slide 26
Results & Performance
All project goals achieved — competition-ready MicroMouse robot
What Worked Well
Key Lessons Learned
17
- Flood-Fill navigated all test mazes without getting stuck
- PD controller maintained ±2 mm straight-line motion
- Gyroscope achieved consistent 90° turns with ±1° accuracy
- WiFi dashboard reduced PID tuning time from hours to minutes
- 3-LiDAR setup reliably detected all maze walls
- Always add voltage protection before connecting the MCU
- Unit test every component before full system integration
- Keep backup critical components on hand
- Live tuning dashboards significantly reduce iteration time
- Sensor fusion outperforms single-sensor approaches
Notes: All goals achieved. 100% maze completion, accurate motion control, live WiFi dashboard. Key lessons around voltage protection and staged testing.

## Slide 27
Future Work & Improvements
Where this project could go next
Speed Optimization
Sprint-phase acceleration profiling
Diagonal movement to cut maze corners
PID auto-tuning via web dashboard slider
Mechanical Upgrades
Lighter PETG or CF-reinforced PLA chassis
Smaller footprint — more agile navigation
±0.5° LiDAR mounting precision bracket
Software Enhancements
A* heuristic layer over Flood-Fill
EEPROM maze persistence across power cycles
Bluetooth mobile config app
18
Notes: Future improvements: speed optimization, mechanical upgrades, software enhancements, and official competition compliance testing.

## Slide 28
Thank You · Questions Welcome
MicroMouse Robot
Interfacing Techniques 2025–2026
19
Notes: Conclusion: all goals met. The robot successfully explores and solves unknown mazes with accurate motion control and live WiFi tuning capability.